## Slide 1: OpenMC Neutronics Analysis of an ABR-1000 Reactor Core
Cal Kaufman
NERS 590 – Advanced Reactor Design

## Slide 2: Contents
Introduction to the ABR-1000
Core Design Description
Approximations
Modeling Methodology
BOC Performance
Depletion Evolution
TRU & Actinide Evolution
Power Distribution
Discussion & Conclusion

## Slide 3: Introduction to the ABR-1000
What is it?
Why it matters
SFRs efficiently fission transuranic (TRU) isotopes from LWR spent fuel, reducing long-term radiotoxicity and heat load of nuclear waste.
Target Performance
Closed fuel cycle with recycled metallic U-TRU-Zr fuel and a target TRU conversion ratio of ~0.7 over a 328.5 EFPD cycle.
1000 MWt pool-type sodium-cooled fast reactor (SFR) developed by Argonne National Laboratory under the GNEP program.

## Slide 4: Core Design Description
379-Assembly Hexagonal Core
78 inner-core + 102 outer-core driver fuel assemblies
114 radial reflector + 66 radial shield assemblies
19 control assemblies (15 primary, 4 secondary)
Assembly pitch: 16.142 cm; 271 pins per assembly
Fuel: U-TRU-10wt%Zr metallic alloy, HT9 cladding
Active core height: 85.82 cm; fuel volume fraction: 39%

## Slide 5: Approximations
Cylindrical Homogenization: 4 annular regions of equivalent area
The hexagonal core is collapsed into concentric annuli of equivalent area. Radial boundaries: Rinner = 78.14 cm, Router = 119.56 cm, Rrefl = 149.94 cm, Rshield = 164.99 cm. Vacuum boundary conditions applied on all outer surfaces. Five axial composition zones represent the burnup-dependent gradient at BOEC.

## Slide 6: Modeling Methodology
Nuclear Data
ENDF/B-VIII.0 continuous-energy cross sections;
Transport Settings
60 batches (20 inactive),
Tallies
8 tallies:
Tfuel = 807 K,
Tcool/struct = 706 K
Depletion Scheme
CECM predictor-corrector integrator via openmc.deplete;
12 geometric timesteps spanning 328.5 EFPD;
20,000 particles per batch;
20×20×20 Shannon entropy mesh for convergence.
total/zone power,
neutron balance,
system leakage,
and 33-group spectral flux.
SFR transmutation chain.

## Slide 7: Beginning of Cycle Performance
BOC keff = 1.04916 ± 0.00070
Benchmark mean: 1.0355 ± 0.0078; deviation of ~1258 pcm, well within the known spread attributable to library differences and geometric modeling.
Competing biases: cylindrical homogenization increases leakage (negative bias), while ENDF/B-VIII.0 and no explicit fission products introduce positive bias.

## Slide 8: Keff Evolution
Reactivity Swing:
Δρcycle = −2415 pcm
Benchmark: −2210 ± 422 pcm
Monotonic decrease driven by 239Pu and 241Pu depletion and accumulation of higher actinide absorbers (240Pu, 244Cm).
EOC keff= 1.02309 ± 0.00066

## Slide 9: TRU Evolution
85.2
kg/cycle
TRU destroyed
94.8
kg/year
TRU consumed
2859.4 kg → 2774.2 kg
ANL reference: 81.6 kg/year (~16% elevated due to positive k-eff bias)

## Slide 10: Actinide Evolution
The depletion of 239Pu is dominant transmutation pathway.
Increases in higher actinide masses, particularly 240Pu, 244Cm, reflect fast neutron capture chains.
Fission exceeds 238U capture production, enabling sustained actinide burning, with a TRU conversion ratio of ~ 0.7

## Slide 11: Power Distribution
Outer core exhibits higher local power density due to higher TRU enrichment
Axially, the power distribution peaks near the core midplane
Inner Core Power: 48.08%
Outer Core Power: 51.92%

## Slide 12: Neutron Spectrum
Fast flux fraction (>0.1 MeV): 0.645 (ANL ref: 0.68)
System leakage: L ≈ 1.13%
(n,2n) on 238U contributes 0.19% of total neutron production
Characteristic of fast-spectrum systems.

## Slide 13: Discussion & Conclusions
Validation
BOC k-eff = 1.04916 (within benchmark spread); reactivity swing = −2415 pcm vs. −2210 ± 422 pcm benchmark mean; TRU consumption = 94.8 kg/year.
Biases
Cylindrical homogenization, ENDF / B-VIII.0 vs. JEFF-3.1 / ENDF / B-VII.0 library differences, and natural Mo pseudo-fission product surrogate.
Next Steps
Full hexagonal lattice; explicit fission product chain; multi-cycle equilibrium analysis; increased particle statistics (≥100,000/step).

## Slide 14: References
C. Grandy et al. Advanced Burner Reactor 1000 MWth reference concept. Technical Report ANL-AFCI-202, Argonne National Laboratory, September 2007. Prepared for the U.S. Department of Energy under Contract No. DE-AC02-06-CH11357.
T. K. Kim et al. Numerical benchmark results for 1000 MWth sodium-cooled fast reactor. In Second Meeting of the SFR Benchmark Task Force of the Working Party on Scientific Issues of Reactor Systems (WPRS), OECD/NEA, Paris, France, February 2012
Md. Hasebul Hasan Niloy et al. Neutronic analysis of ABR-1000 sodium cooled fast reactor with radially and axially heterogeneous core configurations. Annals of Nuclear Energy, 193:110022, 2023.
Paul K. Romano et al. OpenMC: A state-of-the-art Monte Carlo code for research and development. Annals of Nuclear Energy, 82:90–97, 2015.
N. E. Stauff et al. Benchmark for neutronic analysis of sodium-cooled fast reactor cores with various fuel types and core sizes. Technical Report NEA/NSC/R(2015)9,OECD Nuclear Energy Agency, February 2016.
Nicolas Stauff et al. Argonne neutronic assessment of ABR-1000.Technical Report CRADA 2021-21076, Argonne National Laboratory, May 2022.